Critical Design Review (CDR)

Project Description

This project will design and implement a Smarthome lighting and ceiling fan control system. Controls will allow light fixtures to vary their brightness in a dimmable fashion, and ceiling fans driven by single-phase AC induction motors will be speed controllable.

Control messages will be sent wirelessly. The wireless communication will be using the Zigbee Mesh protocol. Xbee Series 2 modules will be used, in API mode and with built-in encryption capability enabled.

Wall “switch” controls will be small LCD touchscreens, communicating with the items they control via wireless command messaging. The LCD will allow the user to select a room, and then which target item in that room to view current status of, or to change it's state. (ie. The selected item in the selected room will get brighter, dimmer, slower, faster, etc.)

The target items being controlled will use a microcontroller as the Zigbee command receiver. Dimmable light fixtures or speed-controllable motor-driven target items will use a common Triac-based circuit to control the target as desired by the user.

A central computer server will log events, control “vacation mode” away events, and act as a gateway for automatic and manual controls sent from distant control devices carried by the home residents. This server will also act as the Zigbee wireless network “coordinator” node, in charge of the Zigbee mesh network. This server will also have an LCD touchscreen panel for

Android smartphones will offer both automatic and manual controls sent via the Linux server, and also a way to remotely view the server's log data in text form. Current status of the home targets will be visible in a GUI which mimics that seen on the LCD touchscreen wall “switches”. The mobile devices will primarily use a GPS based geofence to indicate whether the user is home or away. An alternative control method will be with the use of NFC tags at the front door of the home, so the user can manually swipe his or her mobile device across a tag to manually indicate that they are leaving or returning home. These two control capabilities allow the server to automatically enter and leave an automated, quasi-random “vacation mode”, where it will turn lights on and off at reasonable times to emulate the residents being home for added security from burgulars.

This project will also be designed to allow future expansion, with possibility to add new kinds of target items to control and new types of controls. The intention is to complete a project comparable to popular X-10 systems, but which will send control commands wirelessly instead of signaling over power line. Some example ideas for future additions are garage doors, electronic entry door locks, thermostat HVAC environment control, or safety shutoff for electrics ovens or lab soldering stations, in case you forget to turn them off when you leave home, but these examples are not included in this semester's project effort.

While the ideal would be for the wall “switch” controls to fit into a standard Decora ™ wallplate and housing gang area, and target controls would fit into common ceiling fan wiring canopies or other light fixture wiring boxes, this project during the semester will be made using prototyping computing and interface boards, which will not cleanly fit such common switch housing, and so will not implement a cosmetic ideal. To cosmetically fit into the popular housings would require custom PCB design and assembly to compact the various components used, as well as alternate choice of LCD touch panel of proper size, which may not be supported by the intended Arduino code libraries available, and require software porting to make use of. These additional tasks are beyond the scope of this semester's effort to create a working prototype.

This project evolved from an initial concept fo a wireless controlled light switch, and complexity was added to bring that up to an acceptably complex project for this course.

This project is an individual effort, and does not depend on other projects, nor do other projects depend on this.

Functional Description

Interface Description

The most commonly used interface will be a small LCD touchscreen, mounted about the home (or business) in wall-switch wall-plate locations.
The LCD will display
- A Graphical User Interface to select the room and target device location, view current target state (as the target may be located in another room and not directly visible)
- Control buttons to increase or decrease target brightness or speed, full on or off, or some favorite intensity level for that target.

Material/Resource Requirements

There are three major components of the smarthome system. There are also some general household items, such as light fixures, ceiling fan units, wiring boxes and power cabling which will be required.

Both the controls and the targets in the Arduino class will require an Arduino microcontroller board and the Wireless/SD shield, which holds an Xbee module and possibly a microSD card. The controls will also require an LCD touchscreen/SD shield, and the targets will also require the triac based AC line control circuitry. The target end will also require a couple lights and a ceiling fan to control. An Xbee module will be required for each Arduino and target node. A 2.4inch LCD touchscreen+SD module was chosen so that these prototypes are close to a standard Lenovo Decora™ wall-plate slot. A commercial product would need to refine into a more exact LCD package.

I have not yet purchased components for the triac AC line control circuits, as I will need more time to evaluate available app notes and examples to determine appropriate part numbers to use in this design. I will do this during the weeks leading up to my scheduled time to work on this part of the system, leaving a week or so for shipment and delivery. If delivery is for some reason delayed a little, then I will begin assembly of the Fan and light fixtures with some wiring and electronics enclosures in preparation of the triac circuits coming, and then begin work on the Android app until the AC control components are received.

I already have a couple Arduino Uno boards, have ordered one each of a few items for fast delivery, and ordered additional copies of some items at lower cost with slower delivery. I have now received Wireless+SD shield and LCD touch/SD shield. I also have ordered a few Arduino Due boards, and already have one in possession. Additional Unos and Dues are in shipment from Ebay sellers located in China. I have already received some items from Chinese sellers, and anticipate the remainder of my orders arriving by the end of the first week in October, 2015.

The Linux server will be built using an AMD Gizmo embedded computing board, an 7 inch LCD touchscreen, a USB WiFi dongle, an Msata storage card, and some custom connectivity to the Xbee module.

For the Android class, I will be using the smartphones that My wife and I already own and use. I will also use a home Wifi network router that I already own as the backbone of my simulated internet between the Android devices and the Linux server.

I have acquired a couple simple, inexpensive light fixtures, wall electrical boxes, and an inexpensive ceiling fan unit, to act as my targets to be controlled by this system. I will evaluate whether 2-wire lamp cord is suitable, or if 12-2 Romex should be purchased for the 120V AC line wiring.

Development Plan

The source code, circuit diagrams, documentation, and any other digital data related to this project will be committed and tracked using a Design Management (or Configuration Management in some vocabularies) repository using the GitHub service, located at
https://github.com/amigabill/jhu_EN525.743

I plan to work on the various system components in the following order:

Arduino
- SD card storage (contains some node configuration data)
- Zigbee communication (With PC laptop as coordinator at this point)
- Target control of AC line triacs (with at least some visible output indication, such as a small LED, in place of final triac circuit)
- Touchscreen input events, using some pre-planned location for test “buttons”
- LCD GUI implementation
- Anticipating the possibility that the available libraries I plan to use may not all fit together into an Arduino Uno memory space, I plan to use Due boards for the LCD touch control nodes. Uno's are likely to be suitable for the target nodes, as those do not require LCD graphics related libraries or touch drivers, and will have a smaller memory footprint.
Linux Server (AMD Gizmo embedded project board)
- Zigbee coordinator
- Communicate with targets
- Communicate with wall touchscreens
- Implement event logging
- GUI using WxWidgets library
- Networking with internet, using a home WiFi router to emulate the internet. (Overlaps with Android App communicating with Linux server)
Android smartphone app
- Communicate with Linux Server
- GUI indication of targets current states
- GUI manual control of targets
- NFC tag manual location indications (easier to demo than Geofence)
- GPS Geofence locations (somewhat harder to demo than NFC)

It's important to start with the Arduino targets and controls, as without them there is nothing for a Linux server or Android app to do. The next major priority is the Linux based server, to coordinate the other Zigbee nodes, observe and control target events, etc. This server along with the Arduino nodes then make up the bulk of this project's core functionality. Once the server is complete, then I will implement the triac circuitry to control the AC line to a real target light or fan motor in place of the earlier placeholder status LED. At this point, within the home is a fully functioning system with “real” targets working. Finally, I will move on to implementing the Android app. Should scheduling slip, the Android app is not as critical as the Arduino nodes or Linux server roles in this project, and so if anything should not get completed, this app is the most reasonable choice to be worked on last.

Some modifications may be required to the shields to improve signal quality on Arduino pins used on both modules, such as D4 which is SD_CS on the Xbee/SD shield, and an LCD data pin on the LCD shield. Cutting the D4 and other SD slot traces on the Xbee/SD shield, and not using SD on the Xbee/SD shield can help. The LCD shield has another microSD slot on it, using D10 for SD_CS instead of D4.

The anticipated schedule is shown below:

References

I plan to make use of available libraries as much as possible for various components of the software.
Arduino SD library - https://www.arduino.cc/en/Reference/SD
Arduino TFT Library for LCD panel driver, or relevant equivalent for the LCD controller used - https://www.arduino.cc/en/Reference/TFTLibrary
Adafruit Graphics Core library - https://learn.adafruit.com/adafruit-gfx-graphics-library/overview
Digi Xbee
http://ftp1.digi.com/support/documentation/90000976_W.pdf
http://knowledge.digi.com/articles/Knowledge_Base_Article/What-is-API-Application-Programming-Interface-Mode-and-how-does-it-work
https://github.com/andrewrapp/xbee-arduino
http://ftp1.digi.com/support/utilities/digi_apiframes2.htm
http://arduino.stackexchange.com/questions/1500/how-to-make-xbee-module-interrupt-wake-arduino

WxWidgets (for Linux GUI) - http://wxwidgets.org/

Ltspice
- http://electronicdesign.com/power/model-diacs-and-triacs-ac-line-control
- http://electronics.stackexchange.com/questions/87546/ltspice-mac97a8-triac-model-vgs-error

There are several online app notes and example designs which will be relevant to this project:
Atmel AVR datasheet (Arduino Uno) - http://www.atmel.com/Images/doc8161.pdf
Atmel SAM3 Cortex-M3 datasheet (Arduino Due) -
Triac AC line control:
http://www.freescale.com/files/microcontrollers/doc/ref_manual/DRM039.pdf

Arduino Shield documentation:
Xbee+microSD - https://www.arduino.cc/en/Main/ArduinoWirelessShield
LCD touch+microSD -

1. Project description
  1. High level description of project
  2. Brief description of how your project fits into a larger system, if applicable
  3. Capabilities
  4. Limitations
2. Functional description
  1. Functional block diagrams, and or
  2. State machines, and or
  3. Architectural diagrams
3. Interface descriptions
  1. Internal (within your project)
  2. External (to elements you don’t control, such as public internet or partner project)
4. Material and resource requirements
  1. Everything you need to complete the project
    1. Development tools
      1. Any special build, or installation, instructions
    2. Test equipment
    3. Knowledge base
    4. consumables
  2. Where its coming from?
  3. When is it available?
  4. Items expected of you by other students (team projects)
5. Development Plan and Schedule
  1. Approach
  2. Order of development
  3. Milestones & schedule
  4. For team projects
    1. Clear delineation of responsibilities & dependencies
    2. Clear description of interfaces
    3. Integration and test plan
  5. Risk
    1. Identify known risk areas
    2. Present mitigation plan
    3. Does schedule reflect risk areas?
6. References
  1. Reuse of existing material encouraged, as in real life.
  2. Cite all existing work that will be used in your project
7. Assembly instructions (final project document only)
  1. Instructions to set up development environment
  2. Describe basic steps to assemble from scratch (i.e. bare metal rebuild)
8. Performance and measurement data (final project document only)
  1. Provide screen shots, test data, measurement data as necessary to show functionality of each subsection, and of the entire system.

After the PDR, this document will evolve into your CDR document and then later to the document which satisfies the documentation requirements for this course. It is a living document which will evolve and grow as your project progresses. Both CDR and final document should address, at least, the items outlined above. The evolutionary cycle is outlined below.

- The PDR presentation (MS PowePoint Brief) is a high level description of your project.
- The PDR charts will become the CDR design document (MS Word format), which is a more detailed version that includes any changes you might have made since the PDR. The CDR doc should contain narrative for each section. You will submit this document, but will not present it to the class.
- After CDR submittal, the remainder of the course will be dedicated to development. The development activity will be documented for inclusion in the project document. The CDR document will be updated to reflect changes and expanded to include assembly and performance data.
- The final project document should provide enough detail that any of your peers could modify/improve/incorporate your design without interacting with you.