All radios in same network must have same PAN ID set.

AT Mode
- Needs DH and DL set to assign the destination radio, using atdh and atdl commands
- Broadcast destination address, in DH and DL settings, 0x00000000, 0x0000ffff is broadcast to all radios in same PAN ID
- Specific destination address, in DH and DL settings, goes only to that one receiver.

API Mode
Does NOT need DH and DL set to assign destination radio. This is done within the API frame.
- Broadcast destination address, in the API frame, 0x00000000, 0x0000ffff is broadcast to all radios in same PAN ID
- Specific destination address, in the API frame, goes only to that one receiver.
- Data to send goes into uart TX buffer via Serial.write(), API frame type is 0x10
- Received data in uart RX buffer via Serial.read(), API frame type is 0x90 RX Received

Mixed API and AT modes
- An API mode module can talk to an AT mode module, and vice-versa
- The API or AT mode is how the thing on the serial port (microcontroller, PC etc) talks to the module.
The choice between API and AT has no effect on how radios talk to other radios.

Sending data
- API frame type is 0x10, Transmit Request
- API mode sender puts full frame data into uart TX buffer, from delimiter to checksum, inclusive.
- AT mode sender puts ONLY the payload into uart TX buffer.
- It doesn't matter what mode the receiver isin.

Receiving data
- It doesn't matter what mode the sender was in.
- API receiver receives the full frame at uart RX buffer, from delimiter to checksum, inclusive.
- API frame type is 0x90, RX Received
- AT receiver receives ONLY the payload on the uart RX buffer.